## Slide 1
Seth Petry-Johnson
@spetryjohnson
Don't worry, my content is better than my AI art!
Home Automation Without the Cloud!
Notes: -----------------------------------------------
------- START THE TIMER -------------
-----------------------------------------------
Welcome to Home Automation Without The Cloud!

## Slide 2
Hi, I’m Seth, and I’m too lazy to work a light switch!
I have a dream…
Home Automation Without the Cloud!
Notes: This is me.
For years, I’ve been dreaming about building a truly smart home where everything just sort of does what I want, automatically.

## Slide 3
I want to watch a movie, but I’m already so comfy…
I have a dream…
Home Automation Without the Cloud!
Notes: Maybe I’m sitting on the couch on a bright Sunday afternoon, my cat is on my lap, and I decide I want to watch a movie.
But I’m already really comfortable and getting up to turn off the lights is a real drag.

## Slide 4
Conform to my will!
I have a dream…
Sure thing, boss!
Home Automation Without the Cloud!
Notes: In this dream world of mine, I’d press a single button, or give a single voice command, and the whole environment would shift into a configuration that’s optimized for mid-day movie watching.
The lights would turn off…

## Slide 5
I have a dream…
Sure thing, boss!
Home Automation Without the Cloud!
Notes: … and the window shades would come down to eliminate glare,
(click)
… the TV and speakers would shift into theater mode, and then…
(click)
… a cold beer and a bucket of popcorn would materialize out of nowhere in front of me.

## Slide 6
I have a dream…
Let’s do this!
Home Automation Without the Cloud!
Notes: And through all of that, the cat never had to get off my lap.
That’s the kind of smart, automated home I see in my dreams.
When COVID hit and I needed a hobby, I decided to see how close I could get to my dream using today's technology.

## Slide 7
I have a dream…
Uh, here’s the thing…
Home Automation Without the Cloud!
Notes: Unfortunately, despite all the technology available these days, most people are nowhere close to that level of automation in their homes.

## Slide 8
Sadly, most “smart homes” are kind of dumb
… I'm dumb and don’t know how to do that

Home Automation Without the Cloud!
Notes: We spent almost $75B on home automation in 2021, and yet for most people, the pinnacle of their home automation experience is turning on lightbulbs from their phone, as long as their internet connection is working and as long as no one turned off the power at the wall switch.
(next) I think that’s dumb.

## Slide 9
Sadly, most “smart homes” are kind of dumb
… I'm dumb and don’t know how to do that

Well… crap.
Home Automation Without the Cloud!
Notes: I think it's dumb that all that money and tech is focused on basic use cases that don't provide the rich experience that I'm dreaming of.
Fortunately, though, you CAN do more interesting and useful things, it just requires a little bit of technical skill, a little bit of knowledge, and a little bit of elbow grease.

## Slide 10
Sadly, most “smart homes” are kind of dumb
Allow me to enlighten you…
Awesome! Being dumb sucks!
Home Automation Without the Cloud!
Notes: That brings us to today.
This session is a summary of everything I’ve learned and implemented over the last few years.
I'll show you what’s possible with today’s tech and I'll give you a roadmap to follow if you choose to begin your own home automation journey.

## Slide 11
Today’s agenda
Why so anti-cloud, bruh?
Z-Wave vs Zigbee vs Wi-Fi vs Matter
Getting started with Home Assistant
Remote access
Voice control
Bright ideas for lights, appliances, and more
Home Automation Without the Cloud!
Notes: During this session we’re going to talk about why you should care about local control and execution,
(click)
… the different types of devices and protocols that support local control …
(click)
… and how to use this thing called Home Assistant to manage everything.
(click)
Then I'll show you how I'm using those things to make my home smarter, including adding smarts to my legacy appliances.
(click)
We'll also talk about how you can remotely access your locally-controlled smart home…
(click)
… and how you can use voice control without relying on Alexa or Google.

## Slide 12
Why so anti-cloud, bruh?
Home Automation Without the Cloud!
Notes: To start, lets talk about why you should care about automating your smarthome without the cloud.

## Slide 13
Why so anti-cloud, bruh?
Stuff breaks when cloud services go down
Home Automation Without the Cloud!
Notes: First, I think it’s dumb for your smart home to lose functionality because your Internet connection dropped or because some cloud service is having problems.
A year or two ago the Ring doorbell system went down. Some people had integrated their smart door lock into the Ring app, and they found themselves unable to get into their homes because of an AWS outage.
There was a similar issue when a Google outage took down the Nest ecosystem, and people with Nest thermostats were unable to locally control their A/C until it came back up.
And those were just temporary outages; what happens if the provider of your cloud services goes out of business? I don't want something in my house to stop working just because Google finally decided to kill it off.

## Slide 14
Stuff breaks when cloud services go down
Lackluster attention to security
Why so anti-cloud, bruh?
Home Automation Without the Cloud!
Notes: The second reason I’m anti-cloud is that IoT devices are notorious for having poor security.
You may not care if a Chinese hacker can change the color of your smart lightbulb, but it's a different story when we're talking about cameras and door locks.
And remember that security isn't just about your devices; cloud services require you to log into them, and they collect information about you.
That information has to be stored somewhere, which means it can be stolen.

## Slide 15
Stuff breaks when cloud services go down
Lackluster attention to security
Limited functionality / interoperability
Why so anti-cloud, bruh?
Home Automation Without the Cloud!
Notes: Third, cloud services tend to focus on basic use cases, like turning on a light from your phone.
They don’t typically support more advanced use cases that involve different types and brands of devices working together.

## Slide 16
Stuff breaks when cloud services go down
Lackluster attention to security
Limited functionality / interoperability
User experience
Why so anti-cloud, bruh?
Alexa, it’s movie time!
Say what?
Home Automation Without the Cloud!
Notes: Lastly, I’m anti-cloud because the user experience sucks.
One of the first things I tried on this journey of mine was SmartThings.
I had just created a “movie time” automation to dim all the lights, and as my wife and I were getting ready for a Friday night movie I decided to show off.
(click)
She was reaching for the lights and I said “yo, check this. Alexa, it’s movie time”
(click)
But I got the syntax wrong, so Alexa responds with “I don’t know what you mean”

## Slide 17
Stuff breaks when cloud services go down
Lackluster attention to security
Limited functionality / interoperability
User experience
Why so anti-cloud, bruh?
Uh, Alexa, start the movie time scene!
Home Automation Without the Cloud!
Notes: So I’m like “oops, I mean, Alexa, start the movie time scene”.
(click)
But there must have been some sort of hiccup between my Echo, the AWS network, and the SmartThings network, because nothing happened immediately. I'm just standing there looking stupid.

## Slide 18
Stuff breaks when cloud services go down
Lackluster attention to security
Limited functionality / interoperability
User experience
Why so anti-cloud, bruh?
You’re an idiot ;)
Home Automation Without the Cloud!
Notes: My wife rolls her eyes, turns off the wall switch with a single finger, and sits down on the couch.

## Slide 19
Stuff breaks when cloud services go down
Lackluster attention to security
Limited functionality / interoperability
User experience
Why so anti-cloud, bruh?
You’re an idiot ;)
Hey, where’d ya go?
Home Automation Without the Cloud!
Notes: A moment later I get a notification on my phone from SmartThings saying it can’t reach my light.
Turning off the switch killed the power to the smart bulb, knocking it off the network and making it unavailable by the time SmartThings finally got around to processing the event.

## Slide 20
Stuff breaks when cloud services go down
Lackluster attention to security
Limited functionality / interoperability
User experience
Why so anti-cloud, bruh?
Ok, ok, we get it! Yeesh.
Home Automation Without the Cloud!
Notes: Ok, so enough ranting from my soapbox.
The point is, running your smarthome locally is a key element of that smart home nirvana that I’m dreaming about.

## Slide 21
The land of milk and honey
(my vision of a truly “smart” home)
Ooh, tell us more!
Home Automation Without the Cloud!
Notes: And speaking of that smart home nirvana, let’s take a minute to identify what a truly “smart” home looks like, at least to me.
These are the things that local control will help us achieve.

## Slide 22
The land of milk and honey
(my vision of a truly “smart” home)
Automation is better than control
Ooh, tell us more!
Home Automation Without the Cloud!
Notes: First, I think that automation is better than control.

## Slide 23
The land of milk and honey
(my vision of a truly “smart” home)
Automation is better than control
Home Automation Without the Cloud!
Notes: For example, consider the laundry room in my basement.

## Slide 24
The land of milk and honey
(my vision of a truly “smart” home)
Automation is better than control
Home Automation Without the Cloud!
Notes: To get there, I pass through three distinct areas, each with their own lighting controls.
Controlling those lights from my phone is a neat trick, but it's not very helpful when my hands are full of laundry baskets.
Using my voice is a pain because there are three distinct areas, and giving separate audio commands for each area gets really old really quick.
I could group the lights into a scene, and then use my voice to active the scene, but that only works if a smart speaker can hear me, and it requires training my wife and kids to turn the scene on and off as needed.
And really, I don’t want to control the lights, I want them to be automated.

## Slide 25
The land of milk and honey
(my vision of a truly “smart” home)
Automation is better than control
Home Automation Without the Cloud!
Notes: To do that, I put motion sensors in each area so that the lights
(click) automatically turn on when I enter the room, and
(click) automatically turns off after I leave.

## Slide 26
The land of milk and honey
(my vision of a truly “smart” home)
Automation is better than control
Umm… “motion activated lights” are kind of lame. Is that the best you got?
Home Automation Without the Cloud!
Notes: Of course, motion controlled lights aren’t really a big deal.
I could have bought some cheap, dumb, motion-activated light switches from Walmart and done the same basic thing.

## Slide 27
The land of milk and honey
(my vision of a truly “smart” home)
Automation is better than control
Smart automations beat dumb automations
Motion-controlled lights
- Turn off when you want them on
Home Automation Without the Cloud!
Notes: But those cheap Walmart switches are examples of dumb automations. Each switch only knows about whether or not it senses motion. It doesn't know if any other switches are sensing motion, it doesn't know what time of day it is, it doesn't know if you want it to control the lights at that given moment. That lack of knowledge really limits their usefulness.
For example, after I automated my laundry lights, I decided to add motion based lighting to my living room as well.

## Slide 28
The land of milk and honey
(my vision of a truly “smart” home)
Automation is better than control
Smart automations beat dumb automations
Motion-controlled lights
- Turn off when you want them on
I have to move every 10 minutes!?
Suck it up, buttercup!
- Turn on when you want them off
Home Automation Without the Cloud!
Notes: But then my daughter complained that if she was sitting still on the couch watching TV, the motion sensor would think the room was empty and would turn the lights off.
(click) She’d have to wave her arms in the air every 10 minutes to turn them back on.
(click) By itself that wasn’t a super compelling argument, because in my opinion making kids move their bodies to watch TV is a feature, not a bug.
(click) But I’m really picky about my own TV watching experience…

## Slide 29
The land of milk and honey
(my vision of a truly “smart” home)
Automation is better than control
Smart automations beat dumb automations
Motion-controlled lights
- Turn off when you want them on
- Turn on when you want them off
Home Automation Without the Cloud!
Notes: But I’m really picky about my own TV watching experience…
… and we sit down one night for a family movie, and I dim all the lights for the perfect theatrical experience, and then the moment someone reaches forward to grab their popcorn it triggers the motion sensor, which shoots the lights up to max brightness and ruins it.

## Slide 30
The land of milk and honey
(my vision of a truly “smart” home)
Automation is better than control
Smart automations beat dumb automations
Motion-controlled lights
- Turn off when you want them on
- Turn on when you want them off
This aggression will not stand, man…
Home Automation Without the Cloud!
Notes: It’s one thing to disrupt my daughter’s TV time, but I draw the line at things screwing up my movie night.
Dumb automations are sometimes useful, but other times they just get in the way.
(next) I’m far more interested in making smart automations that are context-aware…

## Slide 31
The land of milk and honey
(my vision of a truly “smart” home)
Automation is better than control
Smart automations beat dumb automations
Context-aware motion control
That’s what I’m talking ‘bout, Willis!
Home Automation Without the Cloud!
Notes: …I’m far more interested in making smart automations that are context-aware.
My daughter wants the lights to stay on when she's watching TV during the day, even if she's still.
I want the lights to stay off if I'm watching a movie at night, even if motion is detected.
Both of us want the lights to turn off automatically when we're done in the room.
We’ll talk more about this in a little bit.

## Slide 32
The land of milk and honey
(my vision of a truly “smart” home)
Automation is better than control
Smart automations beat dumb automations
DGAF what happens to someone else’s computers
Home Automation Without the Cloud!
Notes: Third, I don’t care what happens to my internet connection or to anything else on the Internet.
If my electricity is working, I want my lights to be automated.

## Slide 33
Automation is better than control
Smart automations beat dumb automations
DGAF what happens to someone else’s computers
Works for other people too, not just me
The land of milk and honey
(my vision of a truly “smart” home)
How do we get to this promised land?
Home Automation Without the Cloud!
Notes: Lastly, not everyone in my house is as enthusiastic about this as I am.
My last rule is that other people shouldn’t need a training manual or a fancy phone to navigate my house. Lights and switches should work the way they would expect, and the automations don't get in their way.
(click)
Ok, that’s my vision of a truly smart home, and running everything locally makes these things possible.
But how do we get there?

## Slide 34
Hubs, protocols, and devices
Pick one of these
Pick one of these
Pick as many of these as you want
Open a door
Lights turn on
Home Automation Without the Cloud!
Notes: These are the three ingredients that you need for a basic, locally controlled smart home.
(click)
You need a hub to control everything,
(click)
… you need to choose a protocol that your hub and devices will use to communicate,
(click)
… and you will need at least one device that supports that protocol, such as a bulb or switch or whatever.

## Slide 35
Let's talk about Hubs
Door opened
Turn on lights
Home Automation Without the Cloud!
Notes: Let's talk about hubs first.
The hub is the "brain" of your smarthome. It listens for events and then responds to those events by sending out commands.
When you open a door to your room, the brain tells your light to turn on. Pretty simple.
If this brain lives in the cloud, then you have all of those connectivity and latency issues I want to avoid.

## Slide 36
Let's talk about Hubs
Home Automation Without the Cloud!
Notes: To run things locally, that brain needs to live in your house and on your local network.

## Slide 37
Let's talk about Hubs
Home Automation Without the Cloud!
Notes: As part of my journey, I evaluated 5 different hubs.
Each of these things is capable of acting as that "brain" in your smarthome, but in the end I found one clear winner.

## Slide 38
Let's talk about Hubs
Too cloud centric
Home Automation Without the Cloud!
Notes: I ruled out SmartThings because it was too cloud centric…

## Slide 39
Let's talk about Hubs
Too cloud centric
Too Apple-centric
Home Automation Without the Cloud!
Notes: … and I ruled out HomeKit because it's too Apple centric.

## Slide 40
Let's talk about Hubs
Too cloud centric
Too Apple-centric
Too kludgy
Home Automation Without the Cloud!
Notes: Hubitat is ugly and hard to use….

## Slide 41
Let's talk about Hubs
Too cloud centric
Too Apple-centric
Too kludgy
Too expensive
Home Automation Without the Cloud!
Notes: … and while HomeSeer looks like a really nice product, it's a commercial offering and cost more than I wanted to pay.
Home Assistant, however, was just right for my needs.

## Slide 42
Let's talk about Hubs
Free and open source
Very active community
Monthly releases
Plug-and-play option
Home Assistant Green
$99
Home Automation Without the Cloud!
Notes: Home Assistant is a free, open source home automation hub with a very active community.
The screenshots and examples in this session are all from Home Assistant, but many of the concepts I'll talk about can be applied to the other hubs too.
Home Assistant is free software, but you have to run that software on some sort of computer in your home.
There are many ways to do that.

## Slide 43
Let's talk about Hubs
Plug-and-play option
Home Assistant Green
$99
Home Automation Without the Cloud!
Notes: If you want a plug-and-play, turnkey option then you can buy a product called Home Assistant Green.
This device is designed specifically to run Home Assistant and it comes with everything pre-installed and ready to go.

## Slide 44
Let's talk about Hubs
Raspberry Pi / thin client
Home Assistant Green
$99
Home Automation Without the Cloud!
Notes: But you don't have to buy new hardware, because Home Assistant can be installed on existing hardware you already have.
It can run on a Raspberry Pi or a thin client PC…

## Slide 45
Let's talk about Hubs
Virtual Machine on existing PC
Home Assistant Green
$99
Home Automation Without the Cloud!
Notes: … and you can also download a free Virtual Machine to run on an existing Linux, Mac, or Windows computer.
(click)
Lastly, you can also run it as a Docker container.
Bottom line, everyone in this room should be able to run Home Assistant for free, if they wanted to.

## Slide 46
Let's talk about Hubs
and Protocols
The brain
How the brain talks to stuff
Home Automation Without the Cloud!
Notes: In order for that hub to be useful, it has to be able to communicate with your devices.
Generally speaking, home automation devices communicate over one of 4 different protocols: Zigbee, Z-Wave, Matter, and the ubiquitous Wi-Fi.

## Slide 47
Brains of the smart home
Let’s talk about Hubs
Picking a protocol
Not ideal for local control and automation
The brain
How the brain talks to stuff
Home Automation Without the Cloud!
Notes: Unfortunately, even though it's so widely available, wifi isn’t really a good choice for a locally-controlled smarthome.

## Slide 48
No standard for local control; some devices have local APIs, but are rarely documented.
Picking a protocol
Home Automation Without the Cloud!
Notes: First, there’s no standard that specifies how local control should work on a wifi device.
Some devices expose APIs that you can access over the local network, these APIs are rarely documented.
Typically, those APIs are designed to support the vendor’s app, and the vendor doesn’t want them being called directly by 3rd party integrations.

## Slide 49
No standard for local control; some devices have local APIs, but are rarely documented.
Every device needs its own separate app. Good luck getting different brands of devices to interoperate.
Picking a protocol
Home Automation Without the Cloud!
Notes: From the vendor’s perspective, the need for a device-specific app is the whole point.
They want you to use their app because they want you to register your contact info with them, and they want to collect data on you, and they want to monetize your engagement with that device in any way that they can.
And since every device has its own app, it's hard to integrate different brands and types of Wifi devices together.

## Slide 50
Picking a protocol
No standard for local control; some devices have local APIs, but are rarely documented.
Every device needs its own separate app. Good luck getting different brands of devices to interoperate.
Those apps depend on the cloud and are often insecure.
Home Automation Without the Cloud!
Notes: Lastly, those apps are often poorly implemented and insecure because security just isn't one of the vendor's top priorities.

## Slide 51
Use Wi-Fi devices only when a better protocol isn’t available
Picking a protocol
Home Automation Without the Cloud!
Notes: I’m not saying you can never use wi-fi devices, and I have a couple in my own home.
My point is that you should learn about the other protocols and choose wifi devices only as a last resort.

## Slide 52
Established protocols; widely supported
New kid on the block
Picking a protocol
Home Automation Without the Cloud!
Notes: Excluding wifi, there are three viable protocols that you should know about.
Two of these, Zigbee and Z-Wave, have been around for a long time and are very widely supported.
The third, Matter, is very new.
I'll skip an overly detailed review of each protocol and instead I'll give you this grossly oversimplified summary.

## Slide 53
Lower cost Wifi interference
Interop issues
Not ready for prime time… yet
Picking a protocol
Higher cost Robust and reliable
Home Automation Without the Cloud!
Notes: Zigbee devices are fairly inexpensive, but they share the same wireless frequency as wifi. A busy Zigbee mesh can disrupt wifi signals and vice versa. Additionally, some of the low cost devices can have reliability and interoperability issues.
(click)
Z-wave devices tend to cost a little more, but in my experience are very reliable and feature rich.
(click)
And while Matter has some really laudable goals, it's not quite ready for prime time. It might be the future of the interconnected smart home, but for present day I still recommend Zigbee or Zwave.

## Slide 54
Lower cost Wifi interference
Interop issues
Not ready for prime time… yet
Picking a protocol
Higher cost Robust and reliable
This is an extreme oversimplification. Don't @ me with "well, actually…" 
Home Automation Without the Cloud!
Notes: Again, this is an extreme oversimplification, and any one of these protocols can handle your basic use cases of turning lights on and off. You can even mix and match devices if you want; I personally have a large Z-wave mesh, but I also have a handful of Zigbee devices. Everything is controlled through Home Assistant and for the most part I don't have to think about which device uses which protocol.
However, there IS one technical detail that you should consider.

## Slide 55
Require a radio transmitter / receiver
Picking a protocol
Big promises Not quite there yet
Home Automation Without the Cloud!
Notes: These protocols are all wireless, so to use them you need some way for your Home Assistant box to receive and transmit those wireless signals.
For Z-wave and Zigee, you'll need to get an inexpensive USB dongle that contains the necessary radio. These are plug-and-play and generally integrate very easily into Home Assistant.

## Slide 56
Require a radio transmitter / receiver
Requires a Thread border router
Picking a protocol
Apple TV 4k
Apple HomePod Mini
Amazon Echo smart speakers
Amazon Eero mesh routers
Next Hub / Next WiFi routers
Home Automation Without the Cloud!
Notes: Matter is a little big different. It uses a protocol called Thread, and Thread requires a dedicated device to act as a "border router". The border router is the thing that bridges those wireless signals onto your local network.
The good news is that various Apple, Amazon, and Google devices have Thread built in and can act as that border router, so if you already have one of those devices then theoretically you should be able to run Matter.
If you don't already have one of those devices, however, then you should probably stick with Zigbee or Zwave.

## Slide 57
Hubs, Protocols, and Devices
Let's GOOOOOOOO!
Home Automation Without the Cloud!
Notes: That covers two of the three basic ingredients of a locally controlled smart home.
(click)
But to make anything interesting, we need to add some devices into the mix.
Let's start with the simplest thing to use: a lightbulb.

## Slide 58
Let's talk about Devices
Let's GOOOOOOOO!
Home Automation Without the Cloud!
Notes: This is a Z-wave, RGB lightbulb being controlled through a Home Assistant dashboard.
I can turn it on and off, change the brightness, (click)
and change the color of the LED. I can do this from my computer as well as from my phone.
(click)
Not very exciting yet, so let's add another bulb to the mix.

## Slide 59
Let's talk about Devices
Z-Wave
Wifi
Home Automation Without the Cloud!
Notes: This is interesting because the Living Room bulb uses Z-Wave, but my nightstand bulb is controlled over wifi.
Earlier I said that you should avoid wifi devices when possible, and that's true. But it doesn't mean you can never use them. In this case, someone in the Home Assistant community figured out that this brand of bulb exposes a simple API that can be accessed over the local network. They published an integration for this bulb that allows Home Assistant to show me the exact same user interface as the Z-wave bulb, so as a user of the system I can't really tell a difference.
The problem is that the local API wasn't really designed for 3rd party usage, so this integration could break in the future if the vendor pushes out a firmware update that changes how that API works.
I don't have to worry about that with Zwave.

## Slide 60
Let's talk about Devices
Home Automation Without the Cloud!
Notes: Another benefit of Zwave or Zigbee is that Home Assistant can display a centralized management console for those devices.
Not only can I see everything listed in one place, but I can also edit their configuration settings such as how quickly my lights turn on or off, and what they should do after a power outage.
Since wifi devices have no standard management protocol, you generally won't find a centralized list of them like this.

## Slide 61
Let's talk about Devices
Home Automation Without the Cloud!
Notes: Z-wave and Zigbee give you more than just lightbulbs.
I have a thermostat and temperature sensors so I can track and manage climate controls…

## Slide 62
Let's talk about Devices
Home Automation Without the Cloud!
Notes: … and I also have a Z-wave door lock.
This integration gives me all of the functionality you get from a cloud-based smart lock, but without the subscription fee.

## Slide 63
Let's talk about Devices
These controls are great, but show us the automations, man!
Home Automation Without the Cloud!
Notes: Three years into this, I now have over 150 different devices registered in Home Assistant between bulbs, switches, sensors, TVs, speakers, cameras, phones, etc.
I don't really care about flashy interfaces, so my primary dashboard is very barebones, mostly just a list of toggles and settings.
But these dashboards are totally configurable, so you can make them look really nice if you want. I'll show you an example of a better looking dashboard in a bit.
(click)
So, earlier I said that "automation is better than control", but so far I've only shown you ways of manually controlling devices.
Let's move on and talk about automating some of these things.

## Slide 64
Let's talk about Smart Automations
Lights turn on when someone enters the room
Lights stay on if we're watching TV, but sitting still
Lights stay off when we're watching a movie, even if we move
Lights turn off after everyone leaves the room
Works for me!
Home Automation Without the Cloud!
Notes: For context, let's go back to my living room:
(click) I want the lights to turn on automatically when we first enter the room,
(click) my daughter wants the lights to stay on while she watches TV without waving her arms in the air, and
(click) we both want to the lights to stay off during evening movies.
(click) And finally, I want the lights to turn off automatically when the room is empty.
(click)
Those requirements are a little bit tricky, but if we can pull it off then we'll both be happy.
That's great for me and my daughter, but it turns out that my wife has bad mojo when it comes to technology, and stuff often misbehaves for her in strange ways.

## Slide 65
Let's talk about Smart Automations
Please, make it stop.
Lights turn on when someone enters the room
Lights stay on if we're watching TV, but sitting still
Lights stay off when we're watching a movie, even if we move
Lights turn off after everyone leaves the room
Home Automation Without the Cloud!
Notes: She gets irritated if weird things happen with the lights and I'm not around to fix it.
So to make everyone happy, let's add one more requirement…

## Slide 66
Let's talk about Smart Automations
Yes ma'am.
My wife can disable the automations when they tick her off
Motion detection
Activity recognition
Light control
Kill switch
Lights turn on when someone enters the room
Lights stay on if we're watching TV, but sitting still
Lights stay off when we're watching a movie, even if we move
Lights turn off after everyone leaves the room
Home Automation Without the Cloud!
Notes: … that gives her a way of disabling the automations if they are getting on her nerves.
If we break these requirements down a little bit, we end up with 4 different things to figure out:

## Slide 67
Motion detection
Activity recognition
Light control
Kill switch
Components of Smart Automations
Home Automation Without the Cloud!
Notes: We need a way of detecting if people are in the room or not
(click)
We need a way of detecting what people are doing in the room.
(click)
We need a way of controlling the lights based on those details, and
(click)
We need a kill switch or some other way for my wife to make it all stop.

## Slide 68
Motion detection
Activity recognition
Light control
Kill switch
Components of Smart Automations
Home Automation Without the Cloud!
Notes: Motion detection is easy.
There are battery-powered Z-wave, Zigbee, and Matter-based motion sensors that stick on your walls with adhesive and report their status into Home Assistant.
The batteries in these sensors can last for months, so it's simple to tell which rooms are occupied.

## Slide 69
Motion detection
Activity recognition
Light control
Kill switch
Components of Smart Automations
Home Automation Without the Cloud!
Notes: Activity recognition is more complicated.
The motion sensor tells us if someone is moving within the room, but that's it. It doesn't tell us if we're watching TV during the day, having a family movie night, or doing a puzzle.
In my case, the TV in our living room uses a Roku as its streaming device. There is a Roku integration for Home Assistant that not only lets me control playback, but it also provides… (click)
… diagnostic information, such as which app is currently active.
If the TV is off, then the active app is just "Roku", which tells me it's idle. But if the active app is something else, such as Netflix, that's a pretty clear sign that the TV is being watched.

## Slide 70
Motion detection
Activity recognition
Light control
Kill switch
Components of Smart Automations
Home Automation Without the Cloud!
Notes: The third component to this solution is an ability to turn lights on or off as needed.
The simplest possible thing you can do is buy some Z-wave or Zigbee bulbs for your existing lamps. They are easy to control and can display all sorts of pretty colors, and it requires no specialized skill to install a lightbulb.

## Slide 71
Motion detection
Activity recognition
Light control
Kill switch
Bulbs are neat,
but switches got 'em beat!
Components of Smart Automations
Home Automation Without the Cloud!
Notes: However, I recommend you put in smart switches instead of smart bulbs.
The main problem with smart bulbs is that they need to remain powered at all times. When you turn off a smart bulb, it just turns off the LEDs, but the device itself remains powered and on the network, so that it can receive the commands to turn back on.
If you put one of these bulbs into a lamp or ceiling fixture that's controlled by a switch, and someone in your house flips that switch, then no amount of screaming at Alexa is going to do anything until the switch is flipped back on.
If you replace the switch itself, however, this is a non-issue. Your spouse or your kids or your guests can continue to use the wall switch, like the cave people they are, without affecting your automations.
Additionally, some switches have extra features that can be really useful, which I'll talk about in a minute.

## Slide 72
Motion detection
Activity recognition
Light control
Kill switch
Custom toggle switches in Home Assistant
Components of Smart Automations
Home Automation Without the Cloud!
Notes: Finally, let's talk about the kill switch. This could also be called the "saved Seth's marriage" switch, because it allows my wife and I to peacefully coexist in my evolving house of wonders.
(click)
In Home Assistant, you can create custom toggle switches, and you can then use those toggles in templates and automations.
For instance, I generally set up two control toggles for each room: one controls whether lights turn on automatically, the other controls whether lights turn off automatically.

## Slide 73
Motion detection
Activity recognition
Light control
Kill switch
Components of Smart Automations
Home Automation Without the Cloud!
Notes: Once all 4 of those elements are in place, we can finally create an Automation in Home Assistant to manage the lights.
(click)
Automations start with one or more Triggers. There are many different types of triggers, but in this case I begin the Automation when the motion sensor starts detecting motion.

## Slide 74
Motion detection
Activity recognition
Light control
Kill switch
Components of Smart Automations
Home Automation Without the Cloud!
Notes: Automations can have one or more optional Conditions, which are things that must be true in order for the automation to continue processing.
First, I make sure that the auto-on toggle is enabled. If my wife has turned that flag off, then the automation won't process.

## Slide 75
Motion detection
Activity recognition
Light control
Kill switch
Components of Smart Automations
Home Automation Without the Cloud!
Notes: Next, I check the status of the TV.
If the TV is in use, then I assume that the lights are already set the way the room's occupants want them, and automation exits.

## Slide 76
Motion detection
Activity recognition
Light control
Kill switch
Components of Smart Automations
Home Automation Without the Cloud!
Notes: Lastly, the automation only fires during certain hours of the day.
Sometimes, like when a poorly tested automation incurs the wrath of my wife, I end up sleeping on the couch in this living room. I don't want the cats triggering the motion lights at 3am, so I limit the automation to the primary hours of the day.

## Slide 77
Motion detection
Activity recognition
Light control
Kill switch
Components of Smart Automations
Works for me!
I mean, it's fine…
Home Automation Without the Cloud!
Notes: So when motion is detected, and the kill switch hasn't been activated, and the TV is not currently in use, and it's during the normal waking hours, then the Automation turns on my lamp.
(click)
At this point, I have an automation that keeps my daughter and I happy, and there's a kill switch for my wife to use if things go haywire.
(click)
However, it's still not perfect. My wife is capable of opening Home Assistant on her phone to disable automations that are bothering her, but she doesn't like doing it.
What I really want is some way to enable the kill switch without using a phone app.

## Slide 78
Motion detection
Activity recognition
Light control
Kill switch (no app required)
Components of Smart Automations
Works for me!
I mean, it's fine…
Z-wave switches FTW
Home Automation Without the Cloud!
Notes: I mentioned earlier that Z-wave and Zigbee light switches often have extra features, and one of those features is support for double tap operations.
In my living room, if you single tap the switch it will turn the light on or off, like a normal cave person would expect.

## Slide 79
Motion detection
Activity recognition
Light control
Kill switch (no app required)
Components of Smart Automations
2X
Double-tap "on" disables auto-off toggle
Home Automation Without the Cloud!
Notes: But if you double-tap the "on" switch, it turns the lights on AND keeps them on, by disabling the auto-off automations.

## Slide 80
Motion detection
Activity recognition
Light control
Kill switch (no app required)
Components of Smart Automations
2X
Double-tap "off" disables auto-on toggle
Home Automation Without the Cloud!
Notes: Likewise, double-tapping the "off" switch turns the lights off and keeps them off, by disabling the auto-on automations.

## Slide 81
Motion detection
Activity recognition
Light control
Kill switch (no app required)
Components of Smart Automations
Automatically re-enable after a few hours
OK, you can sleep in the bed now 
Home Automation Without the Cloud!
Notes: The final touch is that I have an automation that re-enables these toggles after a few hours. My wife can double-tap the switch when she enters a room, she can do whatever she wants to do, and then she can leave. She doesn't have to remember to re-enable the automations, because they turn back on automatically.
(click)
Sometimes, when I explain this setup to people, they think its overkill.
But to me, this an example of a near-perfect smart automation. It's context-aware enough to do the right thing at the right time, it doesn't cost me any money or leak any of my information, and it reduces the amount of time I spend sleeping on the couch. Win-win-win.

## Slide 82
Automating Your Smarthome
Motion detection
Activity recognition
Light control
Kill switch (no app required)
Components of Smart Automations
Automatically re-enable after a few hours
That’s better, but…
Notes: The final touch is that I have an automation that re-enables these toggles after a few hours. My wife can kill the automations while she performs some task, and she doesn't have to remember to re-enable them when she's done; it happens automatically.
(click)
This works great when there's a smart light switch or some other physical control that's in a convenient place to act as that kill switch.
But what if you don't have smart switches in convenient places?

## Slide 83
Automating Your Smarthome
Motion detection
Activity recognition
Light control
Kill switch (no app required)
Components of Smart Automations
Automatically re-enable after a few hours
That’s better, but…
Notes: A neat solution is to use NFC tags.
You can get a 20 pack of these for $6, and they make it super easy to trigger automations from wherever you want.
The tags are writeable, and you can…
(click)
… write a value to them using the Home Assistant mobile app. It just uses your phone's NFC chip to write the value, instead of reading it.

## Slide 84
Automating Your Smarthome
Motion detection
Activity recognition
Light control
Kill switch (no app required)
Components of Smart Automations
Automatically re-enable after a few hours
That’s better, but…
Notes: You can also create Automations that are triggered by that tag being read or scanned by a phone with Home Assistant installed.
So, all my wife has to do is tap her phone against one of those tags, and that can turn off automations in the room she's in.
You can even trigger different actions based on which phone scanned the tag, so my wife can tap a tag to disable automations, and I can tap that very same tag to re-enable them.
Finally, these tags do not require a power source. There's no battery to change, there's no cable running down the wall, the NFC chips obtain the power they need from the phone that scans them. All you need is a tiny piece of adhesive to affix the tags where you want them and you're done.

## Slide 85
Automating Your Smarthome
Motion detection
Activity recognition
Light control
Kill switch (no app required)
Components of Smart Automations
Automatically re-enable after a few hours
OK, you can sleep in the bed now
Notes: This is a great example of why it's easier to implement smart, context-aware automations with a platform like Home Assistant instead of a cloud-based platform like Google Home or SmartThings.
Getting all of these devices to work together, combined with the logic that's very specific to my own home, would be difficult if not impossible. And even if you could make it would, you'd probably have at least one subscription fee in there somewhere.
I not only keep my marriage healthy, but I do it without a monthly fee.

## Slide 86
Let's talk about Appliances
I haz the dumbs.
Home Automation Without the Cloud!
Notes: That covers lights and switches and motion sensors, so let's move on to another interesting use case.
(click)
I have a standard old dumb washing machine. It has no internet connectivity of any kind.
Our laundry room is located in the basement, which is…
(click) waaaaaay far

## Slide 87
Let's talk about Appliances
I iz far away.
Home Automation Without the Cloud!
Notes: … . waaaaaay far away from our general living area.
On occasion we'll run a load of clothes…

## Slide 88
Let's talk about Appliances
Is the washer done yet?
Z-Wave power plug
Home Automation Without the Cloud!
Notes: … and then find ourselves wondering if it's time to move them to the dryer yet.
Now, we could walk all the way downstairs to take a look, but as you've probably guessed by now, that's not my style.
(click)
What is my style is buying a Z-wave enabled power plug, like this one.

## Slide 89
Let's talk about Appliances
Sweet! Time to dry.
No power being used = Washer not in use
Home Automation Without the Cloud!
Notes: This plug reports the amount of power being used into Home Assistant, and I can use that to determine if the washer is running or not.
That's neat, but instead of constantly checking my dashboard, I'd rather be notified when it's time for me to take action.

## Slide 90
Let's talk about Appliances
Sweet! Time to dry.
Home Automation Without the Cloud!
Notes: To do that, I set up notifications that trigger when the power usage goes from a non-zero number back to zero.
That means the washer was running but has now stopped, so there's probably a sopping wet mess of clothing that needs moved.

## Slide 91
Let's talk about Appliances
Sweet! Time to dry.
Home Automation Without the Cloud!
Notes: I perform those notifications in a few different ways.
First, I send a push notification to my phone. Nothing super exciting there.

## Slide 92
Let's talk about Appliances
Sweet! Time to dry.
Home Automation Without the Cloud!
Notes: However, I'm not the only one that does laundry, so when a load is finished I also make a text-to-speech announcement over our Alexa devices.
We have smart speakers in our kitchen, living room, and master bedroom, so anyone in those rooms will hear a friendly audible message that the laundry needs moved to the dryer.
Now, playing audio messages in bedrooms is tricky. I would happily be woken up at 3am by an alert about a water leak, but my wife isn't too keen on being woken at 3am just because an overnight load of laundry is done.

## Slide 93
Let's talk about Appliances
Sweet! Time to dry.
Home Automation Without the Cloud!
Notes: To manage that complexity, I created a custom, reusable script that handles the text-to-speech notifications. It's like a utility function in your code that lets you reuse logic in multiple places.
This script is smart enough to choose which devices will play the message based on the time of day and the message type.
A water leak notification plays on all speakers at any time of day, but laundry alerts don't play in the bedroom during sleeping hours.

## Slide 94
Let's talk about Appliances
Whelp, that's an easy choice.
"Smart washer" with crappy app that relies on cloud services
$1000+
Smart plug + dumb washer,
bespoke notifications $20
Home Automation Without the Cloud!
Notes: If you buy a "smart appliance" with built-in notifications, you're paying a lot of money and you're limited to whatever notifications that app supports.
Doing it locally gives me more control and saves me some money at the same time.

## Slide 95
Let's talk about DIY options
Whelp, that's an easy choice.
"Smart washer" with crappy app that relies on cloud services
$1000+
Smart plug + dumb washer,
bespoke notifications $20
Home Automation Without the Cloud!
Notes: So far, everything I've shown you has used off-the-shelf, plug-and-play devices and has been really easy to set up.
Next, I want to show you how you can save some money and handle even more complex scenarios if you're willing to put in just a little bit of extra effort.
I'm going to use my garage as an example. We have a lot of expensive tools in our garage, and I want to keep them secure.

## Slide 96
Let's talk about DIY options
When door is open:
Visual status indicators in the house
Video recordings of motion
Distance sensor $2
Home Automation Without the Cloud!
Notes: Specifically, I want passive indicators inside the house that tell us if the garage door is open, so that it's easy to see if someone forgot to close it.
Secondly, I want a camera to take recordings of the garage so that if there's ever a theft, we'll have evidence.
But, I don't need gigabytes of videos of my kids getting soda from the garage fridge, so I only want to save those videos if motion occurs while the garage door is open. If the garage door is closed, nothing gets saved.
Lastly, I want to store those videos on a hard drive located inside the house, so that a thief can't steal the video evidence along with the tools.
This would be nearly impossible if I was relying on cloud services for all of these things, but because I'm running everything locally it only required a few extra components.
(click)
First, I bought a simple distance sensor for $2 so that I can track the status of the garage door.

## Slide 97
Let's talk about DIY options
When door is open:
Visual status indicators in the house
Video recordings of motion
Distance sensor $2
Closed 10 feet to floor
Home Automation Without the Cloud!
Notes: That distance sensor is mounted to the garage ceiling, and when the garage door is closed it measures the distance from the ceiling to the floor, which is about 10 feet.

## Slide 98
Let's talk about DIY options
When door is open:
Visual status indicators in the house
Video recordings of motion
Distance sensor $2
Open 10 inches to door
Home Automation Without the Cloud!
Notes: When the door is open, it rolls back along the track and underneath the distance sensor, which then measures the distance from the ceiling to the rolled up door, which is about 10 inches.
That distance measurement can therefore tell me whether or not the door is open.

## Slide 99
Let's talk about DIY options
When door is open:
Visual status indicators in the house
Video recordings of motion
Distance sensor $2
Motion sensor $2
Raspberry Pi + camera $20
Home Automation Without the Cloud!
Notes: For the motion sensing I could have used one of those Z-wave sensors I showed earlier, but since I'm already going the DIY route I bought a much cheaper sensor for another $2.
Since these are just basic electronic components, not stand-alone devices, they need some sort of controller to power and control them, so…
(click)
… I also bought a cheap Raspberry Pi Zero to be that controller. I added a camera for the Pi to record videos.

## Slide 100
Let's talk about DIY options
When door is open:
Visual status indicators in the house
Video recordings of motion
Motion sensor $2
Distance sensor $2
Raspberry Pi + camera $20
Home Automation Without the Cloud!
Notes: Wiring those sensors to the Raspberry Pi was easy.
(click)
I didn't need any a soldering iron or any special equipment, just a few of these jumper wires from Amazon or Microcenter.

## Slide 101
Let's talk about DIY options
Motion sensor $2
Distance sensor $2
Raspberry Pi + camera $20
Python libraries make it super easy
Home Automation Without the Cloud!
Notes: Getting the Pi to talk to the sensors is also pretty easy. The Pi can execute Python scripts, and there are Python libraries for interfacing with those sensors, so I just need a few lines of code in a loop to continually monitor the motion sensor and garage door status.
Based on those values, I can decide whether or not to record a video and send it to the file server in my basement.

## Slide 102
Let's talk about DIY options
{ state: "Detected" }
Home Automation Without the Cloud!
Notes: That's cool and all, but I also want to get that data into Home Assistant so that I can refer to those sensor values elsewhere in my system.
(click)
The typical way of doing that is using something called MQTT, which is a very lightweight, publish/subscribe protocol that is widely used in home automation.
You can install an MQTT broker directly into Home Assistant, and with a new more lines of Python we can…
(click)
… send a JSON payload to that broker, which automatically triggers Home Assistant to update.
So, we now have a Raspberry Pi tracking motion and garage door status and then pushing those values into Home Assistant.
The final requirement is some sort of visual indicator inside the house telling us when the door is open.

## Slide 103
Let's talk about DIY options
{ state: "Detected" }
Home Automation Without the Cloud!
Notes: Once again, it's Z-wave light switches for the win. Some of the switches I have come with a configurable color bar on the switch itself.
Normally, this is blue, and the brightness of the bar indicates the amount of dimming currently applied.
(click)
But when the garage door state changes from closed to open, I change the color bars on a few switches throughout the house to a different color. That makes it really easy for anyone walking by the front door, for instance, to see that the garage is open.
The brightness of the bar doesn't change, it still reflects the dimming level of the light it's connected to, but the color grabs our attention and communicates status.
(click)
And when the door closes, I reset the light bar back to its default color.
Simple, but effective.

## Slide 104
Let's talk about Control Panels
Psst! Hey, you need a control panel? Everyone's got one, it will make you cool. You can stop using it whenever you want…
Home Automation Without the Cloud!
Notes: For my final example, lets talk about control panels.
(click)
If you spend any amount of time on home-automation Reddit, you'll notice that a fancy control panel, located on some wall of your house and available for anyone to use, is pretty much a de-facto requirement to be one of the cool kids.
The good news is, any device that can display a web browser or run an Android app can function as a control panel when used with Home Assistant.
Lots of people will mount an old ipad to the wall, or use a raspberry pi with a spare monitor, but I….

## Slide 105
Let's talk about Control Panels
Home Automation Without the Cloud!
Notes: … use this little Android-powered display that can be mounted in place of a standard, 2-gang wall switch.
This panel is running the Home Assistant app and displaying a dashboard that I created.
This dashboard pulls together everything I've talked about so far. It allows anyone in my home to see the status of key systems and to take control of lights and scenes, all without taking out a phone.

## Slide 106
Let's talk about Control Panels
Home Automation Without the Cloud!
Notes: The garage door and front door icons turn orange when they are open or unlocked, so it's easy to see if those items need secured.

## Slide 107
Let's talk about Control Panels
Home Automation Without the Cloud!
Notes: The laundry icon turns yellow when the laundry machines are in use…

## Slide 108
Let's talk about Control Panels
Home Automation Without the Cloud!
Notes: … and then turn into a blinking orange icon when the load is done and needs someone to take action.

## Slide 109
Let's talk about Control Panels
Home Automation Without the Cloud!
Notes: If any of my water sensors detect a leak, then I show that as a big red blinking alert.

## Slide 110
Let's talk about Control Panels
Home Automation Without the Cloud!
Notes: And lastly, I show the salt level in my water softener. When it's full the icon is green, but as it runs low…
(click)
the color changes to yellow and then red, so that we know we need to buy more salt.
I'm sharing this panel partially because I think it's cool, but also because it demonstrates one final Home Assistant technique that I want to cover, and that's…

## Slide 111
Let's talk about Control Panels
Home Automation Without the Cloud!
Notes: … the use of templates for advanced configuration.
The vast majority of Home Assistant configuration can be done through visual tools, but most features can be toggled into a YAML editor where you can manipulate the thing directly.
(click)
And most of those YAML configurations support the use of Templates to provide property values.
I use templates to control the colors of my dashboard icons, to map numeric states into textual explanations, etc.
Templates are a really powerful feature. They can have conditional logic, they can calculate values, they can even call custom code to interface directly with hardware devices.
The cloud based commercial offerings don't have anything nearly as powerful.

## Slide 112
Quick recap
Smart Lights (motion sensor + Roku integration + kill switch)
Smart Washer (Power-sensing plug + custom notifications)
Smart Garage (Raspberry Pi + sensors + Python + MQTT)
Control Panels (Home Assistant dashboard + tablet + templates)
Home Automation Without the Cloud!
Notes: I just showed you four different real-world examples of how I've added smart, context-aware automations to my own home, without using cloud services.
You can keep it simple and use off the shelf devices, or you can go down the rabbit hole of DIY sensors and controllers. It's entirely up to you.

## Slide 113
Let's talk about remote access
Home Automation Without the Cloud!
Notes: But what about remote access?
No matter how awesomely automated your home is….

## Slide 114
Bye super awesome smart home. I miss you already!
I thought that bossy guy would never leave!
Let's talk about remote access
Home Automation Without the Cloud!
Notes: … sooner or later you’re going to have to leave that house and go out into the world.
Let’s say you leave in a hurry for vacation, get a few miles down the road, and have that… (next) sinking feeling that you left the lights on, or the garage door open, or whatever else.

## Slide 115
By default, you can’t access your local network from the Internet
Did I leave the garage door open?
Let's talk about remote access
I thought that bossy guy would never leave!
Home Automation Without the Cloud!
Notes: … sinking feeling that you left the lights on, or the garage door open, or whatever else.

## Slide 116
Dynamic DNS
Port Forwarding
Let's Encrypt
By default, you can’t access your local network from the Internet
Did I leave the garage door open?
Let's talk about remote access
Home Automation Without the Cloud!
Notes: If you’re running everything locally, then you can’t connect to Home Assistant unless you’re on the same local network.
As soon as you drop off wifi and onto your cellular network, you’ll lose access because your cell phone can't reach devices on your private network.

## Slide 117
Dynamic DNS
Port Forwarding
SSL Certificate
You can fix that with a little effort…
Did I leave the garage door open?
Let's talk about remote access
Home Automation Without the Cloud!
Notes: You can DIY a solution to those problems if you're comfortable with Dynamic DNS services and port forwarding on your router.
On the other hand, if you want it to Just Work, you can do what I do, and…

## Slide 118
Dynamic DNS
Port Forwarding
Let's Encrypt
Shut up and take my money!
Let's talk about remote access
… or just pay for it
"Home Assistant Cloud" plugin
Ah-ha! I knew you'd need the cloud for something!
Home Automation Without the Cloud!
Notes: … pay $6 a month for the Home Assistant Cloud plugin. This plugin automates all of those networking details and provides a secure tunnel into your instance for easy remote access.
(click)
I do see the irony in recommending a cloud-based service in an anti-cloud session, but I make an exception for this one.
(click)
This is the only subscription fee I have, and I'm happy to support this product. The remote access is a bonus.
Also, I am not dependent on this service. If it goes down, all I lose is remote access from my phone; all of my automations and devices will continue to work just fine.

## Slide 119
Dynamic DNS
Port Forwarding
Let's Encrypt
Let's talk about voice control
"Home Assistant Cloud" plugin
Dude, I need my Alexa integration. It's a deal breaker.
Seamless Alexa integration
Home Automation Without the Cloud!
Notes: That brings us to voice control.
Alexa integration is super convenient, and for many people the convenience of voice control outweighs my arguments about privacy and latency. For those people, losing voice control might even be a total dealbreaker.
The good news is that you do NOT need to give up voice control if you set up Home Assistant.

## Slide 120
Dynamic DNS
Port Forwarding
Let's Encrypt
Let's talk about voice control
"Home Assistant Cloud" plugin
Dude, I need my Alexa integration. It's a deal breaker.
Seamless Alexa integration
Home Automation Without the Cloud!
Notes: That Home Assistant Cloud plugin ALSO provides an Alexa integration, so you can talk to Alexa, and then Alexa talks to the Home Assistant cloud service, which then sends commands to your local instance.
That's great, as long as you already have a bunch of Alexa devices and you're OK with Amazon processing your speech.

## Slide 121
Dynamic DNS
Port Forwarding
Let's Encrypt
Let's talk about voice control
"Home Assistant Cloud" plugin
Dude, I need my Alexa integration. It's a deal breaker.
Seamless Alexa integration
Home Automation Without the Cloud!
Notes: You can choose which devices are exposed to Alexa and which ones aren't…

## Slide 122
Dynamic DNS
Port Forwarding
Let's Encrypt
Let's talk about voice control
"Home Assistant Cloud" plugin
Dude, I need my Alexa integration. It's a deal breaker.
Seamless Alexa integration
Home Automation Without the Cloud!
Notes: … and you can also enable two-way communication, which means that Home Assistant will notify Alexa when devices change state.
This is nice if you have people that want to use the Alexa app to control your devices because their states will be synchronized between the two different apps.

## Slide 123
Dynamic DNS
Port Forwarding
Let's Encrypt
Let's talk about voice control
"Home Assistant Cloud" plugin
Home Automation Without the Cloud!
Notes: And although I've been focusing on Alexa, the Home Assistant Cloud plugin also supports Google Assistant integration.

## Slide 124
Dynamic DNS
Port Forwarding
Let's Encrypt
Let's talk about voice control
"Home Assistant Cloud" plugin
Home Automation Without the Cloud!
Notes: That's great and all, as long as you have a bunch of Alexa devices and you're OK with Amazon processing your speech.
However, Nabu Casa, which is the company behind Home Assistant, has a vision of a privacy-first approach to voice control. They've been putting a ton of effort into making it possible to take Amazon totally out of the picture.

## Slide 125
Keeps your audio private
Not affected by internet outages
More control over the process
Let's talk about local voice control
Home Automation Without the Cloud!
Notes: But I'm not a big fan of letting big, for-profit corporations listen in on my kitchen, living room, or bedroom.
And on top of the privacy benefits, running a local voice assistant can be faster and more reliable than relying on the cloud.

## Slide 126
Let's talk about local voice control
Home Automation Without the Cloud!
Notes: I only have 45 minutes today so I don't have time to do a deep dive on voice control, so I'm going to skip straight to the conclusion.
To do local voice control you need a device that can recognize a wake word and send it to Home Assistant, and you need a service that can parse the voice recording into Home Assistant commands.
The device part is easy: the company that manages Home Assistant recently released a hardware device that comes pretty close to Alexa devices in terms of microphone quality. This is technically a preview edition and I expect the hardware to get even better over time.

## Slide 127
Let's talk about local voice control
Home Automation Without the Cloud!
"Home Assistant Cloud" plugin => Simple voice control
ChatGPT => Conversational voice control, for $
Ollama => Conversational voice control, for free
Notes: By default, that device comes pre-configured to use Home Assistant Cloud for processing. It works really well, as long as you give the commands in the right syntax.
(click)
You can also hook it up to ChatGPT for processing. This gives you far more conversational voice control, at an added usage cost.
(click)
Or, you can do what I do. I run a private LLM on a machine in my basement, and I use that to process my voice commands. It gives me the same conversational approach that ChatGPT does, but it's fully local and free.

## Slide 128
Let's talk about local voice control
Hogwarts, lumos!
Home Automation Without the Cloud!
Notes: One of the best parts about local voice control is that you can set up custom sentences to do some really cool stuff.
For example, my wife loves Harry Potter and LEGO, so for Christmas one year I bought her the big LEGO Hogwarts Castle.
She added a light kit that adds all of these little LED lights in the rooms and parapets of the castle.
In the Harry Potter movies, the spell for conjuring light is "Lumos".
So as a party trick, I hooked up that light kit to Home Assistant so that if anyone says…
(click)
"Hogwarts, lumos", then…

## Slide 129
Swoon
Let's talk about local voice control
Hogwarts, lumos!
Home Automation Without the Cloud!
Notes: … the light kit turns on and lights up the castle.
I got serious Husband of the Year points for that automation.

## Slide 130
What else can you do?
Home Assistant Cloud (remote access + Alexa)
Voice Assistants (local voice control)
M5 Atom Echo (cheap mics w/ 1st class support)
Home Automation Without the Cloud!
Swoon
Hogwarts, lumos!
Notes: Back at the start I told you that I'd show you what's possible with a locally controlled smarthome, and so far we've really only scratched the surface.
Very quickly, here a few more things I'm doing without cloud services.

## Slide 131
What else can you do?
Only $13!? Sweet!
Home Assistant Cloud (remote access + Alexa)
Voice Assistants (local voice control)
M5 Atom Echo (cheap mics w/ 1st class support)
Home Automation Without the Cloud!
Notes: I'm tracking my electrical usage, broken down by individual circuit.

## Slide 132
What else can you do?
Only $13!? Sweet!
Home Assistant Cloud (remote access + Alexa)
Voice Assistants (local voice control)
M5 Atom Echo (cheap mics w/ 1st class support)
Home Automation Without the Cloud!
Notes: I also monitor my water meter, so I know how much water we're using and if we have any leaks anywhere.

## Slide 133
What else can you do?
Home Automation Without the Cloud!
Notes: I can monitor my security cameras, the humidity in my 3d filament storage boxes, even the battery levels of my battery-powered sensors.
There's very little you can't do locally, and I'm not paying subscription fees for any of this.

## Slide 134
DIY sensors / custom HA integrations
bit.ly/LocalSmarthomeFTW
Pick a local hub (Home Assistant, etc)
Pick a protocol for your devices to use
Get some devices that use that protocol
Home Assistant Cloud for remote access + Alexa
RaspPi + Python + MQTT for DIY stuff
seth@petry-johnson / @spetryjohnson
Make smart automations that do cool stuff (but don't forget the kill switch!)
Home Automation Without the Cloud!
Local voice control if you have the right hardware (and you're OK with an 80% solution)
Notes: Here's a roadmap for getting started with your own smart home.
This QR code and bitly link go to my Github repo containing these slides, plus detailed notes on the things I've done and links to the resources I used.
If you decide to get started in this crazy world, drop me a line and let me know!